## Slide 1: Advanced C++ Internals: Chapter 3A Architecture Primer (ARM64)
ZACOCPPINT
Notes: “A” chapters indicate a client specific requirement; in this case A=Architectural

## Slide 2
Architecture Primer (ARM64)
Learning Journey:
  Introduction
  Introducing ARM64 architecture
  ARM64
  ARM States
  ARM64 Registers
  ARM64 Assembly Language
  Comparison: x86/64 vs. ARM64
  C++ to ARM example
  Summary
  Appendices:
  Useful links
Learning Outcomes:
  Must be able to describe basic register model of ARM64
  Should be able to describe basic ARM64 assembly language instruction types and give examples of each
  Could be able to read and interpret basic ARM64 assembly language extracts.
Notes: This implementation provides a primer for ARM64 etc.

## Slide 3
Introduction
Using a binary tool such as Ghidra allows us to reverse engineer programs written in such languages as C, C++ etc.
If native decompilation tools have been built, code analysis will try to reconstruct the original source code.
However, the binary’s machine code (disassembled into native assembly language) is also viewable
In the absence of decompilation, disassembly may be the only option.
This relies on being able to read and interpret the underlying instructions
And how they interact with the CPU and memory respectively.
Notes: This short chapter focuses on ARM64 architecture.
Note.
The specific platform (hardware, CPU architecture and operating system/distribution/version) are selected by the client and may be revised in future versions.

## Slide 4
Introducing ARM64 Architecture
The chosen architecture for this course is ARM64
Also known as AArch64
There are various chip revisions, but few compatibility issues
This is a 64-bit version of the ARM architecture
Designed by ARM Holdings
Compatible with existing ARMv8-A architecture and the A32 and T32 instructions sets
ARM64 family primarily used on devices such as:
tablets
Smartphones
Single board computers (SBCs)
embedded systems, etc*.
Notes: * Due to its efficiency in terms of overall performance/cost ratio and (relatively) low power consumption.

## Slide 5
ARM64
ARM64 has several key advantages over its 32-bit predecessor, including:
Larger register set
Enhanced performance
Better support for virtualization
More flexibility and scalability for different application and platform types, e.g. embedded to high-performance servers

## Slide 6
ARM States
ARMv8 introduced 64-bit architecture
but maintains compatibility with existing 32-bit implementations
It supports two different execution states:
*GPR = General Purpose Register
AArch32
Has access to 32-bit GPRs*
Can only use A32 and T32 instruction sets
AArch64
Has access to 64-bit GPRs*
Compatible with ARMv7-A
Can only use A64 instruction set A64 is a new set of 32-bit instructions which…
Execution state is either A32 or T32
Has access to larger virtual address space
Notes: Technical Notes
A32 is simply the 32-bit instruction set which covers the usual range of low-level operations you’d expect.
T32 are 32-bit instructions which have the benefit of higher code density, whilst slightly degrading performance. This is using a technology called “Thumb-2”; this dates to ARMv4T.
Code density is simply a metric which describes how compactly a solution can be encoded in assembly language, typically involving number, size and complexity (i.e. decode and execution cycles) of instructions involved. This usually impacts performance, memory usage and power consumption of the processor.
Any ARM compiler toolchain will build (or target, if you prefer) executable images for either AArch32 or AArch64 state; this typically may involve the use of a cross-compiler and the installation of some additional packages on the Operating System to run them.
This means, depending on the target that instructions will either be A32+T32 OR A64.
If the CPU state and received instructions are mismatched, problems will occur, e.g. an Exception level, memory segmentation fault etc.
Further Reading:
https://gcc.gnu.org/onlinedocs/gcc/AArch64-Options.html

## Slide 7
ARM64 Registers
The register set is somewhat simplified:
GPRs (General Purpose Registers) | 31 x0  x30 64-bits w0  w30 (lower 32-bits) | x30 (aka “LR”) Link Register GPR “x” registers may have predefined uses in function calls, exception handling etc.
Floating point and SIMD Registers | 32 v0 to v31 128-bits | Aliases for: 64-bit (d0  d31) 32-bit (s0  s31)
Special Registers | PC: Program Counter NZCV Register APSR: Application Program Status Register ELR: Exception Link Register SYS: System Register | Negative, Zero, Carry, Overflow etc.
Other Registers | SP: Stack Pointer (“x31”) LR: Link Register FP: Frame Pointer (“x29”) | To stack top (LIFO) Return address for functions Accessing local variable and parameters
Notes: Technical Notes
SIMD stands for Single Instruction, Multiple Data. ARM’s implementation uses NEON extension.
A type of architectural feature favouring parallelism; same operation on multiple data items, simultaneously, e.g. for vectorization etc.
D prefix = doubleword register; floating-point double-precision
S prefix = single-precision registers
ARMv8 is used inside a Raspberry Pi 4, for example.

## Slide 8
ARM64 Assembly Language
Sample categories and instructions:
Data Transfer | Load Store | ldr x0, [x1] str x2, [x3]
Arithmetic | Add Subtract | add x5, x6, x7 sub x5, x6, x7
Logic | And | and x9, x8, x7
Control Flow | Unconditional branch Conditional branch (post-cmp) | b label b.eq label b.ne label
Function Call | Call Return | bl function ret
Conditional | cset | x10, eq
Floating Point | Add | fadd d0, d2, d3
SIMD | Vector Add | fadd v0.4s, v1.4s, v2.4s
Notes: Other texts may use different categorizations for the instruction set; these are suitably broad so should map to other competing architectures/families, e.g.
ARM documentation would describe Data Transfer as “Register load and store”, Control Flow as “Branch and control” etc.
Further reading:
https://developer.arm.com/documentation/dui0801/a/Overview-of-AArch64-state/A64-instruction-set-overview?lang=en
However, it’s obviously beyond the scope of the program to teach you the full ARM64 assembly language - that’s a week in itself - but we’ll assume some basic familiarity with concepts such as registers, opcode, operands etc. That should make progress here relatively painless.
Further reading:
(No date) Documentation – Arm Developer. Available at: https://developer.arm.com/documentation/#cf-navigationhierarchiesproducts=Architectures,CPU%20Architecture (Accessed: 31 December 2023).

## Slide 9
Comparison: x86/64 vs. ARM64
Here’s a comparison of Intel x86 and ARM64:
section .data
num1 dd 0xA ; Hexadecimal representation of 10
num2 dd 0x7 ; Hexadecimal representation of 7
result dd 0 ; Placeholder for the result
section .text
global _start
_start:
; Add the numbers
mov eax, [num1]
add eax, [num2]
; Square the result
imul eax, eax
; Store the result
mov [result], eax
; Exit the program
mov eax, 1 ; syscall number for sys_exit
xor ebx, ebx ; exit code 0
int 0x80 ; call kernel
x86-64

## Slide 10
Comparison: x86/64 vs. ARM64
Here’s a comparison of Intel x86 and ARM64:
.global _start
.section .data
num1: .word 10
num2: .word 7
result: .word 0
.section .text
_start:
; Add the numbers
ldr w0, num1
ldr w1, num2
add w2, w0, w1
; Square the result
mul w2, w2, w2
; Store the result
str w2, result
; Exit the program
mov x8, 93 // syscall number for sys_exit
mov x0, 0 // exit code 0
svc 0 // call kernel
ARM64
Notes: Both examples assume Linux environments and take a few liberties with assembly file layouts etc.
Note the mixed use of 32-bit and 6-bit registers in this sample/
A very quick overview of mnemonics used here (we’ll be seeing a lot more of them, don’t worry):
ldr – load register from address
add – add(!)
mul – multiply
str – store register value into address
mov – move from source (right) to destination (left)
svc – supervisor call (to the OS)
As you can see, all sensibly named.
After all, “mnemonic” is from the ancient Greek word "mnēmōn," which means "mindful" or "remembering." 

## Slide 11
C++ to ARM Example
Using ARM GCC
int cube_it(int n) {
return n * n * n;
}
ARM64
cube_it(int):
push {r7}
sub sp, sp, #12
add r7, sp, #0
str r0, [r7, #4]
ldr r3, [r7, #4]
mul r3, r3, r3
ldr r2, [r7, #4]
mul r3, r2, r3
mov r0, r3
adds r7, r7, #12
mov sp, r7
ldr r7, [sp], #4
bx lr
Notes: Here’s a quick outline of ARM assembly language produced by GCC compiler (default options)
The code has been colour-coded to reflect the 3 different “phases” of the code, i.e.
Dealing with the function call and supplied argument/parameter
Performing the cubed operation
Returning execution back to the caller
Have a read through and see what you can interpret…
Technical note.
“push” and “pop” stack operations are only shortcuts for memory operations which use “sp” in the address part of the instruction, e.g.
push {r7}
Is actually…
str r7, [sp, #-4]
i.e. this instruction stores the contents of register r7 into the memory location pointed to by the stack pointer minus 4 bytes.

## Slide 12
C++ to ARM Example
Using ARM GCC
Note the use of the “W” (32-bit view) registers and the sp
int cube_it(int n) {
return n * n * n;
}
ARM64
_Z7cube_iti:
sub sp, sp, #16
str w0, [sp, 12]
ldr w0, [sp, 12]
mul w1, w0, w0
ldr w0, [sp, 12]
mul w0, w1, w0
add sp, sp, 16
ret
Notes: Here’s a quick outline of ARM assembly language produced by GCC compiler (default options)
The code has been colour-coded to reflect the 3 different “phases” of the code, i.e.
Dealing with the function call and supplied argument/parameter
Performing the cubed operation
Tidying and returning execution (and effectively the calculated value) back to the caller
Have a read through and see what you can interpret.
Essentially, we are cubing a value passed into register w0.
Let’s start by saying that “_Z7cube_iti” represents our C++ function’s mangled name, created by the Itanium C++ ABI (used by both GCC and Clang).
The ABI (Application Binary Interface) defines how different pieces of binary code can interact correctly with each other, much as an API with source code. This includes practicalities such as memory layout and alignment, specifying the calling conventions, whether registers or the stack are used for arguments, how return values are managed and even who is responsible for tidying the stack after the call. Basically, it enables (for example) Rust programmers to call C library functions etc. Other popular examples of ABI include SysV ABI and Microsoft’s x64 ABI.
_Z: This prefix starts almost all mangled names in GCC and indicates that what follows is a mangled name
7cube_it: This part decodes as follows:
  7 indicates that the next 7 characters are part of the name.
  “cube_it” is the name itself, referring to the cube_it function.
i: Similarly, this part is decoded as:
  “i” indicates that the function parameter is a single integer.
So, for example you should be able to interpret a C++ mangled name such as “_Z6add_meif”
Now, let’s tackle the code, line-by-line:
sub sp, sp, #16 This allocates 16 bytes on the stack by decrementing the stack pointer. This is done to reserve space for storing values temporarily.
str w0, [sp, 12] The value in register w0 is stored at memory address sp + 12. This places the value on the stack at the 12-byte offset.
ldr w0, [sp, 12] The value that was just stored on the stack is loaded back into w0.
mul w1, w0, w0 The value in w0 is multiplied by itself, effectively squaring it, and the result is stored in register w1.
ldr w0, [sp, 12] The original value from the stack is loaded back into w0 again.
mul w0, w1, w0 The squared value in w1 (which is w0 * w0) is multiplied by the original value in w0, resulting in w0^3 (cubing the original value). The result is placed back in w0.
add sp, sp, 16 The stack pointer is restored by adding 16 to it, undoing the space allocated earlier.
ret The function returns, with the cubed value in w0.
Any questions, feel free to ask.

## Slide 13
C++ to ARM example
However, things quickly get complex as C++’s library is utilised, even on the simplest example…
#include <iostream>
int main()
{
std::cout << "Hello, world!" << std::endl;
return 0;
}
ARM64
.LC0:
.string "Hello, world!"
main:
stp x29, x30, [sp, -16]!
mov x29, sp
adrp x0, .LC0
add x1, x0, :lo12:.LC0
adrp x0, _ZSt4cout
add x0, x0, :lo12:_ZSt4cout
bl std::basic_ostream<char, std::char_traits<char> >& std::operator<< <std::char_traits<char> >(std::basic_ostream<char, std::char_traits<char> >&, char const*)
mov x2, x0
adrp x0, _ZSt4endlIcSt11char_traitsIcEERSt13basic_ostreamIT_T0_ES6_
add x1, x0, :lo12:_ZSt4endlIcSt11char_traitsIcEERSt13basic_ostreamIT_T0_ES6_
mov x0, x2
bl std::basic_ostream<char, std::char_traits<char> >::operator<<(std::basic_ostream<char, std::char_traits<char> >& (*)(std::basic_ostream<char, std::char_traits<char> >&))
mov w0, 0
ldp x29, x30, [sp], 16
ret
Notes: And, of course, this is with demangled identifiers, otherwise
bl std::basic_ostream<char, std::char_traits<char> >& std::operator<< <std::char_traits<char> >(std::basic_ostream<char, std::char_traits<char> >&, char const*)
would probably read:
bl _ZStlsISt11char_traitsIcEERSt13basic_ostreamIcT_ES5_PKc

## Slide 14
C++ to ARM Overview/
Breakdown
Function prologue
Save registers on the stack
Prepare args for std::out << “Hello, world!”
Load addresses into registers
Call the overloaded << operator for std::out and const char*
Passing address of std::out and the string
Set up the frame pointer
Prepare args for std::cout << std::endl
Call the overloaded << operator for std::ostream& and the manipulator
Function Epilogue
Set return value (0)
Restore x29 and x30 from stack
Return from function
Notes: Like many traditional function calls, low-level code is mainly a question of:
Prologue (setting stuff up)
Payload (doing something)
Epilogue (tidy up before returning to the caller)
This simple example shows us this format and allows us to explore the various registers being used in the available architecture.
You do need to remember that values passed to functions aren’t always explicitly heralded and many op codes will update registers which are then in turn implicitly used in the next instruction.
Technical notes.
Common ARM64 register conventions used here are:
x0 to x7: Used for passing arguments to functions and receiving return values.
x29: Frame pointer (fp).
x30: Link register (lr).
sp: Stack pointer.
These aren’t always referenced explicitly in an opcode, e.g. look at “ret” (return) for example.

## Slide 15
ARM Breakdown
The function’s “prologue”; sets up the stack frame for main.
Saves frame pointer and link register
Sets up the frame pointer
Mnemonics
stp store pair
mov move
.LC0:
.string "Hello, world!“
main:
stp x29, x30, [sp, -16]!
mov x29, sp
Defines the "Hello, world!" string literal which is stored in the read-only data section of executable.
ARM64
ARM64
Notes: Other things to know here:
.LC0 (label)
main (function name) as entry point
sp = stack pointer (register)
Obvious questions:
Significance of x29, x30?
Significance of -16?
Significance of “!” appended?
Answers:
x29 is commonly used as the frame pointer (fp).
x30 is the link register (lr), which holds the return address.
-16 is representing a 16 byte-decrement (fp and lr registers take up 8 bytes each, of course)
The exclamation mark “!” indicates that the stack pointer is updated (pre-increment).

## Slide 16
ARM Breakdown: step 2
This code loads the address of the “Hello, world!” string into register x1
adrp x0, .LC0
add x1, x0, :lo12:.LC0
ARM64
Then loads the address of std::cout into register x0
adrp x0, _ZSt4cout
add x0, x0, :lo12:_ZSt4cout
ARM64
And then calls the overloaded operator<< for std::basic_ostream and const char *
bl std::basic_ostream<char, std::char_traits<char> >& std::operator<< <std::char_traits<char> >(std::basic_ostream<char, std::char_traits<char> >&, char const*)
ARM64
Notes: Other things to know here:
Opcodes included are:
adrp = load page address (upper 48 bits)
add = add
bl = branch with link; calls a function and saves return address in x30

## Slide 17
ARM Breakdown: step 3
Moves the resulting std::ostream object back into x2 register for next operation…
ARM64
mov x2, x0
adrp x0, _ZSt4endlIcSt11char_traitsIcEERSt13basic_ostreamIT_T0_ES6_
add x1, x0, :lo12:_ZSt4endlIcSt11char_traitsIcEERSt13basic_ostreamIT_T0_ES6_
ARM64
mov x0, x2
ARM64
Loads the address of std::endl into register x1
Prepares the std::ostream object for its next operation…

## Slide 18
ARM Breakdown: final steps
Calls the overloaded operator<< function for std::basic_ostream and the std::endl manipulator
ARM64
bl std::basic_ostream<char, std::char_traits<char> >::operator<<(std::basic_ostream<char, std::char_traits<char> >& (*)(std::basic_ostream<char, std::char_traits<char> >&))
mov w0, 0
ldp x29, x30, [sp], 16
ARM64
ARM64
ret
Sets the return value for the main function (0) using immediate value. Then restores the frame pointer and link register (respectively, from stack) and then updates the sp.
Returns control to the calling function, implicitly using x30 (link register)
Notes: Additional notes:
ldp = load pair
This particular example loads x29 and x30 from the address pointed to by sp. Increments sp by 16 bytes after the load ([sp], 16); popping the stack of those addresses.

## Slide 19
Summary
  ARM64 is a powerful, efficient, and low consumption CPU, ideal for SBC’s and mobile devices.
  ARM64 instruction set is clean and (relatively) simple to learn, consisting of the typical:
  Data transfer (register and RAM)
  Arithmetic
  Logic
  Conditional/unconditional branches
  Function call and return mechanisms
  ARM64 has a relatively straightforward register model
  But some general-purpose registers have multiple reserve uses, depending on instruction mode active
  So, care is required when interpreting: context is king!
  Conversion for x86-64 is relatively painless…
  although not without its challenges!

## Slide 20: Any questions?

## Slide 21: Appendices
Notes: Some additional information you may find useful…

## Slide 22
Useful resources
Websites and online resources
ARM Architecture Reference Manual for ARMv8-A (64-bit) publicly released (no date) Architectures and Processors blog - Arm Community blogs - Arm Community. Available at: https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/arm-architecture-reference-manual-for-armv8-a-64-bit-publicly-released (Accessed: 31 December 2023).
(No date) Documentation – Arm Developer. Available at: https://developer.arm.com/documentation/#cf-navigationhierarchiesproducts=Architectures,CPU%20Architecture (Accessed: 31 December 2023).
Arm Architecture Reference Manual for A-profile architecture (PDF). Available at: https://developer.arm.com/documentation/ddi0487/ja/ (Accessed: 31 December 2023).
(No date) AArch64 Options (Using the GNU Compiler Collection (GCC)). Available at: https://gcc.gnu.org/onlinedocs/gcc/AArch64-Options.html (Accessed: 1 January 2024).
Thomas, D. (no date) DaveSpace. Available at: https://www.davespace.co.uk/arm/introduction-to-arm/ (Accessed: 31 December 2023).

## Slide 23: Review of Chapter’s Learning Outcomes

## Slide 24
Learning Outcomes
Learning Outcomes:
By the completion of this chapter, you…
Must be able to describe basic register model of ARM64
Should be able to describe basic ARM64 assembly language instruction types and give examples of each
Could be able to read and interpret basic ARM64 assembly language extracts.
Please review these learning outcomes at chapter's end.